## Slide 1
Eavesdropper
Listens + collects in-air frames
Collects own CSI
Victim:
Generates traffic
Collects own CSI??
WAP
For wireless communication with victim
Internet
Visited servers are YouTube, Netflix, Stan, etc.
Example Attack Setup

## Slide 2
Victim
Generate traffic
Eavesdropper
Collect CSI
Capture traffic
WAP
Wireless 2.4GHz RF
WPA2 encrypted (ssid:pwd known)
Internet
Example Attack Setup

## Slide 3
Victim
Generate traffic
Eavesdropper
Collect CSI
Use RFMON
Capture traffic
WAP
Channel 11, bandwidth 20MHz
Transmit power is “auto”
WPA2 encrypted (ssid:pwd known)
Internet
Synchronisation
Python socket programming – victim sends traffic generating info and eavesdropper receives messages to start/store/record captures accordingly.
Example Experiment Setup
Capture data storage
Store in 64GB SD cards on Pi’s. Periodically transfer data to a larger HDD/server.
Generate traffic & synchronise captures

## Slide 4
Victim
Eavesdropper
WAP
Channel 11, bandwidth 20MHz
Transmit power is “auto”
WPA2 encrypted (ssid:pwd known)
Internet
Synchronisation
Example Experiment Setup - Interfaces
collect CSI
collect WLAN
gen traffic
socket sync
socket sync
bcm43455c0
RTL8812BU
RTL8812AU
CAT6 – auto MDI-X
CAT6 – auto MDI-X

## Slide 5
Use nmcli
Generate traffic
Experiment Items Explanation
Hardware
OS
Item
Usage
Reason
Browsing automation framework on Python (and others). Works with Chrome, FireFox, etc. drivers.
Can stream videos.
64bit version. Is used arbitrarily. Can use another OS if there is good reason to.
2-core CPU custom built PC. It is using a Linux OS
nmcli is the NetworkManager client. It allows a user to connect, disconnect, reconnect, and manage network settings (e.g. default channel, gateway).
Victim Items

## Slide 6
Collect CSI
Experiment Items Explanation
Hardware
OS
Item
Usage
Reason
32bit ARM version works with Nexmon CSI *and* with RTL8812bu WNIC chipset monitor mode. I’ve written install instructions in 0_setup.
Lightweight and versatile. Pi 4 is preinstalled with WiFi chip supported by Nexmon CSI and we use a USB RTL8812bu WNIC.
To collect the CSI from the eavesdropper’s end. This may be useful in processing/refining features from the captured traffic data. Must be noted that this is the CSI from the eavesdropper’s receiver though, not the victim’s.
Eavesdropper Items
Capture traffic
Listening and capturing all WiFi frames in air with PyShark (TShark wrapper for Python). We can decrypt the WPA2 encryption because we know the key to get the network and transport layer info.

## Slide 7
Victim
Generate traffic
Use RFMON
Eavesdropper
Collect CSI
Use RFMON
Capture traffic
WAP
Channel 11, bandwidth 20MHz
Transmit power is “auto”
WPA2 encrypted (ssid:pwd known)
Internet
Synchronisation
Two-way python socket chat to signal when to start, stop, and metadata info about the capture.
Experiment Development
Need to automate login to YouTube, Netflix and Stan. Sometime ads come up and sometimes video quality is different (360p vs 720p)
Capture data storage
Store in 64GB SD cards on Pi’s. Periodically transfer data to a larger HDD/server.
Key
Developed
Ongoing development
Starting development
I can capture CSI but need to analyse and get insights from it (understand CSI patterns better)